## Slide 1
ADAPTIVE CRUISE CONTROL ROBOT
A Build Guide for a Sensor-Driven, PID-Controlled Follower Robot
ESP32 · HC-SR04 · MPU6050 · L298N · PID Control

## Slide 2
Project Overview
What is Adaptive Cruise Control?
Standard cruise control holds a constant speed. ACC intelligently adjusts speed to maintain a safe, pre-defined distance from the vehicle ahead.
How Real Vehicles Do It
Radar or LiDAR on the front grille bounces waves off the lead car. Time-of-flight gives distance; if the lead car slows, the ECU commands the brakes and throttle to decelerate.
How Our Robot Mimics It
An HC-SR04 plays radar, the ESP32 plays ECU, and instead of brakes it adjusts PWM to the L298N driver — speeding up or slowing the DC motors via a PID loop or an AI model.
System Architecture
Inputs
Distance from HC-SR04, tilt/acceleration from MPU6050
Processing
ESP32 running a PID controller or an AI inference model
Outputs
PWM signals to the L298N driver, commanding the DC motors

## Slide 3
Core Components — Sensing & Control
ESP32
3.3V logic · ~500mA peak
The robot's brain. A dual-core 32-bit MCU that runs the control code, reads sensors, and generates PWM. Strictly 3.3V — 5V on a pin can destroy it.
HC-SR04 Ultrasonic
5V · ~15mA
Acts as the radar. Emits a 40kHz pulse from Trig and reads the echo on Echo; distance is derived from time of flight. Struggles with soft or angled surfaces.
MPU6050
3.3–5V · I2C (SDA/SCL)
Accelerometer + gyroscope that detects tilt, bumps, and slopes using MEMS capacitance sensing, feeding the control loop extra context.

## Slide 4
Core Components — Drive & Power
L298N Motor Driver
Up to 35V, 2A/channel
A heavy-duty H-Bridge switch that supplies motor current the ESP32 can't provide directly, and lets current reverse for forward/reverse driving. Drops ~2V from battery to motors.
DC Motors + Gearbox
Lorentz force
Convert electrical energy into torque: current through a coil in a magnetic field creates rotational force that turns the wheels.
Battery Pack
2x 18650 Li-Ion, 7.4V
Powers the whole system. Two 18650 cells in series are recommended over a 9V battery, which lacks the capacity this build needs.

## Slide 5
Power System
Two 18650 Li-Ion cells in series (3.7V × 2)
7.4V
Nominal voltage
8.4V
Fully charged
2500mAh
Capacity
~3.5 hrs
Estimated runtime
Current Draw
Motors: 2 × ~250mA running (stall up to 1.5A) ESP32 + sensors: ~200mA Total average: ~700mA
Protection
Always use a battery holder with a built-in protection circuit (BMS) to prevent discharging the 18650s below 3.0V per cell, which permanently ruins them.

## Slide 6
Robot Workflow
The robot runs an infinite loop — constantly sensing, thinking, and acting.
1
START
Power on
→
2
INIT
Set up ESP32 pins, I2C bus; init MPU6050 & HC-SR04
→
3
SENSE
Trigger HC-SR04, read Echo, calc distance; read MPU6050 tilt
→
4
FILTER
Apply a moving-average filter to smooth distance spikes
→
5
DECIDE
Compare filtered distance to target via PID / AI
→
6
ACT
Send PWM signals to the L298N to drive the motors
7. REPEAT — loop back to SENSE, continuously

## Slide 7
Distance Control & Filtering
< 10 cm
Emergency Stop
Object too close — speed = 0 immediately
30 cm
Safe Distance
Target distance — robot matches lead speed
> 100 cm
Max Following
Object far — robot cruises at top speed
Distance Calculation (Time of Flight)
Distance = (Speed of Sound × Time) / 2
Speed of sound at sea level ≈ 343 m/s (0.0343 cm/µs)
The sound wave travels to the object and back, so the raw time-of-flight is halved.
Moving Average Filter
Filtered = (x₁ + x₂ + ... + xₙ) / n
Ultrasonic readings occasionally spike to "0" or "400cm" from missed echoes.
Keeping the last 5 readings and averaging them smooths out these erratic jumps.

## Slide 8
PID Control
The industry-standard closed-loop control method — calculates an error and outputs a motor speed.
u(t) = Kp·e(t) + Ki∫e(τ)dτ + Kd·de(t)/dt
P
Proportional (Kp)
Reacts to the present error. Far from 30cm → drive fast; close → drive slow. Can cause overshoot on its own.
I
Integral (Ki)
Looks at past error, summing steady-state error over time to nudge the robot if it stalls just short of target.
D
Derivative (Kd)
Predicts future error from the rate of change of distance, acting as a brake to prevent overshoot.
Tuning by trial and error:
Set Ki and Kd to 0; raise Kp until the robot oscillates around the safe distance.
Raise Kd to dampen the oscillation so it settles smoothly.
Raise Ki slightly if the robot stops just short of the target.

## Slide 9
AI / Machine Learning Integration
Instead of classical PID, ML can map sensor inputs directly to motor outputs.
Option 1: Edge Impulse Classification
Data collection: record ultrasonic + MPU accelerometer arrays Classes: "Too Close", "Safe Distance", "Too Far" Deployment: exported as an Arduino library; ESP32 runs inference and sets motor speed from the winning class
Option 2: Regression Model
Instead of discrete buckets, regression predicts a continuous PWM speed (0–255) from features like current distance and rate of change of distance.
Gives smoother speed transitions than classification, which tends to produce jerky, stepped changes.
Recommendation
For a beginner, PID is the standard and most educational approach. If you do use AI, prefer Regression — Classification tends to cause jerky, stepped speed changes.

## Slide 10
Calibration & Testing
Sensor Calibration
HC-SR04:
Measure an object exactly 20cm away with a ruler. Adjust the 0.034 multiplier in code until the Serial Monitor reads exactly 20cm.
MPU6050:
Place the robot on a flat surface. Raw X, Y, Z should read 0, 0, 1g — the deviations are your offsets to subtract in software.
Testing Checklist
Bench-test sensors: no motors connected — wave a hand in front of the sensor and confirm distance changes on the Serial Monitor
Bench-test motors: wheels off the ground, force analogWrite(enA, 255) — both should spin forward; swap L298N wiring if one runs backward
Integration test: on the floor, walk in front of it — does it follow, and stop when you stop?
Golden Rule
Never combine sensors and motors on the first power-up. Validate each subsystem in isolation, then integrate one piece at a time.
Order of operations
Calibrate HC-SR04 distance reading
Zero the MPU6050 offsets
Bench-test sensors alone
Bench-test motors alone (wheels raised)
Full integration test on the floor

## Slide 11
Troubleshooting
Problem | Likely Cause | Solution
ESP32 randomly resets/reboots | Voltage drop from motors starting up | Power ESP32 from a separate buck converter, or add a large capacitor across the power rails
Robot stutters / shakes | PID Kp is too high (overshoot) | Decrease Kp; increase Kd slightly
Motors hum but don't spin | PWM speed is below the motor's deadband | Add a minimum baseline speed in code (e.g. if speed > 0, speed += 50)
Distance reads 0cm randomly | Ultrasonic echo timed out | Implement a software filter to ignore 0 readings

## Slide 12
Future Improvements
Once the base robot works, consider these engineering upgrades:
Wheel Encoders
The control loop is currently "open-loop" for the motors — we guess that a PWM of 150 equals a certain speed. Wheel encoders measure actual wheel RPM, enabling a cascaded PID loop: the distance PID outputs a target RPM, and a speed PID achieves it.
Sensor Fusion
Combine HC-SR04 distance with MPU6050 accelerometer data using a Kalman Filter to predict where the lead vehicle is, even when the ultrasonic sensor temporarily misses a ping.

## Slide 13
Final Deliverables
Through this guide, you now have:
A complete architectural overview of an ACC system
A detailed pin mapping and wiring strategy for voltage compatibility
A structural workflow and flowchart logic
The mathematical foundation of PID control
A starter codebase demonstrating proportional control
Testing, calibration, and troubleshooting protocols
Take your time with the wiring, build the circuit incrementally, and test each component alone before combining them into the final control loop. Good luck with your build!